## Slide 1: Discrete Math Chapter 8
Computer Logic

## Slide 2: Chapter 8 Overview
8-1 Boolean Algebra Structure
8-2 Logic Networks
8-3 Minimization

## Slide 3: Notes of Chapter 8
In this chapter, we will learn how to design CPU circuits.
Chapter 8 is based on chapter 1; make sure you don’t skip chapter 1 before learning chapter 8.

## Slide 4: 8-1 Boolean Algebra Structure

## Slide 5: Boolean Algebra
Boolean algebra is the branch of algebra in which the values of the variables are the truth values true and false, usually denoted 1 and 0, respectively. (Domain and codomain of Boolean Algebra is {0, 1}.)
Instead of elementary algebra, where the values of the variables are numbers and the prime operations are addition and multiplication, the main operations of Boolean algebra are conjunction, disjunction and negation.
For example, in Boolean Algebra, 1 + 1 is 1, since it means ”True or True”. The disjunction of 2 true values would be true as well; therefore, 1 + 1 = 1.

## Slide 6: Boolean Algebra
Claude Elwood Shannon (1916 – 2001) was an American mathematician, electrical engineer, and cryptographer known as "the father of information theory". Shannon founded information theory with a landmark paper, "A Mathematical Theory of Communication", which he published in 1948.
He also founded digital circuit design theory in 1937, when—as a 21-year-old master's degree student at the Massachusetts Institute of Technology (MIT)—he wrote his thesis demonstrating that electrical applications of Boolean algebra could construct any logical numerical relationship. Shannon contributed to the field of cryptanalysis for national defense during World War II, including his fundamental work on codebreaking and secure telecommunications.

## Slide 7: Definition of Boolean Algebra
A boolean algebra is a set B on which are defined 2 binary operations + and · , and one unary operation ‘ and in which there are 2 distinct elements 0 and 1, such that the following properties hold for all :
(commutative properties)
(associative properties)
(distributive properties)

## Slide 8: Definition of Boolean Algebra
(identity properties)
(complement properties)
A simple way to understand boolean algebra is by
Thinking of addition as “or”, and multipcliation as “and”.
Thinking of 0 as false, and 1 as true.

## Slide 9: Example 8-1-1
Prove that
holds in boolean algebra by using the definition.

## Slide 10: Example 8-1-2
Prove that
holds in boolean algebra by using the definition.

## Slide 11: The Uniqueness of the Complement
For is an element of a Boolean Algebra B, the element ’ is called the complement of (the term is from the set theory). The complement of satisties
+ ’ = 1 and = 0
Also, the ’ is the unique element with these 2 properties. (Which means no other element in B would satistfies both 2 properties at the same time. If we find an element that satisfies both properties, then must equal to ’.)
To prove that ’ is unique, we assume that is an element in B with properties + = 1 and = 0.

## Slide 12: The Uniqueness of the Complement
Then,
= 1 = =
Therefore, we know that ’.
With this theorem known, we can now prove the De Morgan’s Law in Boolean Algebra. We can now proceed to prove:
(Double Negation)
and (De Morgan’s Law)

## Slide 13: Proof I
Does really equals to in boolean algebra? If acts like the complement of , then is . What element acts like the complement of ? According to the uniqueness of the complement, the complement of , let’s call it k, must statisfies:
and
First, does equal to 1? According to the defintion 5, the + of element and the complement of is 1. Therefore, = 1.
Second, does equal to 0? According to the defintion 5, the of element and the complement of is 0. Therefore, = 0.
Then, according to the uniqueness of the complement, we know that .

## Slide 14: Proof I
Now, we are ready to prove and .
First, does really equal to ? We know that is the complement of . Therefore, if then:
1. = 1
2. = 0
Both statements must be true. In the following 2 examples, we will prove that both statements are true.

## Slide 15: Example 8-1-3
Prove that
holds in boolean algebra by using the definition.

## Slide 16: Example 8-1-4
Prove that
holds in boolean algebra by using the definition.

## Slide 17: Proof II
Now, we have proved that We would prove is true now.
Does really equal ? We know that is the complement of . Therefore, if then:
1. = 1
2. = 0
Both statements must be true. In the following 2 examples, we will prove that both statements are true.

## Slide 18: Example 8-1-5
Prove that
holds in boolean algebra by using the definition.

## Slide 19: Example 8-1-6
Prove that
holds in boolean algebra by using the definition.
*. Here, we finished the proof of De Morgan’s Law in boolean algebra.

## Slide 20: Example 8-1-7
Prove that
holds in boolean algebra by using the definition.

## Slide 21: 8-2 Logic Networks

## Slide 22: And Gate and Or Gate
Consider the following circuit:
and are switches that can be turned on or off. Now, both switches are off. If we turn on both swtiches, then we will see the light.

## Slide 23
Now, for this circuit, we can write down the relations between switches and output.
 |  | Output | Picture
0 | 0 | 0 | 
1 | 0 | 0 | 
0 | 1 | 0 | 
1 | 1 | 1 | 
 |  | Output | Picture
0 | 0 | 0 | 
1 | 0 | 0 | 
0 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 24: And Gate and Or Gate
The relations of the switches and the output turn out to behave like the Boolean Algebra operation We can present this circuit as Boolean Algebra equation:
= Output
This logical circuit is called the “And Gate”, which means that, in order to get output to be 1, both swithces and have to be turned on.
When drawing the circuit, it’s presented as:

## Slide 25: And Gate and Or Gate
Consider the circuit on the right; and are switches that can be turned on or off. Now, both switches are off.
If we turn on one of the switches, then the light will be turned on.

## Slide 26
Now, for this circuit, we can write down the relations between switches and output.
 |  | Output | Picture
0 | 0 | 0 | 
1 | 0 | 1 | 
0 | 1 | 1 | 
1 | 1 | 1 | 
 |  | Output | Picture
0 | 0 | 0 | 
1 | 0 | 1 | 
0 | 1 | 1 | 
1 | 1 | 1 | 

## Slide 27: And Gate and Or Gate
The relations of the switches and the output turn out to behave like the Boolean Algebra operation ＋We can present this circuit as Boolean Algebra equation:
= Output
This logical circuit is called the “Or Gate”, which means that, in order to get output to be 1, swithces or has to be turned on.
When drawing the circuit, it’s presented as:

## Slide 28: Not Gate
The ”Not Gate” is also know as the inverter. This circuit behaves like the Boolean algebra unary operation ‘.
When drawing the circuit, it’s presented as:
Now, we know that circuits can be represented as Boolean Algebra, and each Boolean Algebra equation (or Boolean expression) has a corresponding logical circuit. Let’s learn this concept from some examples:

## Slide 29: Example 8-2-1
Draw a logical network for Boolean expression .

## Slide 30: Example 8-2-2
Draw a logical network for Boolean expression .

## Slide 31: Example 8-2-3
Recall from example 8-1-7, we proved that
’
.Draw the circuits of and verify that it is equivalent to ’.

## Slide 32: Example 8-2-4
Try to simplify the circuit below.

## Slide 33: Build Boolean Expression
From chapter 1 and 8, all we have been doing is to contruct the truth table from a boolean expression. However, can we build a boolean expression from a truth table?
For example, what boolean expression is associated with the following truth table? (Think about it, do you have any good idea?)
x1 | x2 | Output
1 | 1 | 1
1 | 0 | 0
0 | 1 | 1
0 | 0 | 0

## Slide 34: Build Boolean Expression
Building a boolean expression from a given truth table is a lot trickier than contructing a truth table from a given boolean expression.
Luckily, someone had already figure it out. The most 2 common approaches to find the boolean expression from a given truth table are:
Disjuctive Normal Form (DNF, or a.k.a. Sum of Products)
Conjuntive Normal Form (CNF, or a.k.a. Product of Sums)

## Slide 35: Disjunctive Normal Form
The concept of DNF is quite simple. By looking at how the truth table get 1 as output, we infer the boolean value of x1 and x2. For example:
To get 1 as output, it has to be either ( is 1 and is 1) or ( is 0 and is 1). Therefore, we can write
*. This is why DNF is also known as the “Sum of Products”.
x1 | x2 | Output
1 | 1 | 1
1 | 0 | 0
0 | 1 | 1
0 | 0 | 0

## Slide 36: Disjunctive Normal Form
The boolean expression perfectly matches the truth table: (If we verify both of them carefully)
By applying what we learned in chapter 8-1, we know that
= ( + ) = 1 =
Therefore, this output of the truth table is only controlled by , regardless the value of .
x1 | x2 | Output
1 | 1 | 1
1 | 0 | 0
0 | 1 | 1
0 | 0 | 0

## Slide 37: Conjuctive Normal Form
The concept of CNF is quite simple, and very similar to DNF. In DNF, we check the 1s in the output of the truth table. In CNF, we would check the 0s in the output of the truth table. For example:
To produce 0s, we need either ( is 1 and is 0) or ( is 0 and is 0).
x1 | x2 | Output
1 | 1 | 1
1 | 0 | 0
0 | 1 | 1
0 | 0 | 0

## Slide 38: Conjuctive Normal Form
Therefore, we can write
Then, by using De Morgan’s law, we can do negation on both sides of the equation, then:
Now, the boolean expression is in a form of “Product of Sums”. This is why CNF is known as “Product of Sums”.

## Slide 39: Conjuctive Normal Form
Last but not least, by applying what we learned from 8-1, we can do:
Then, we know that the output of the truth table is only controlled by , regardless the value of . No matter if we choose DNF or CNF, we will end up having the same conclusion.
How do we know which one to choose? Well, it depends on which one is easier to solve the problem. Let’s learn from the examples below.

## Slide 40: Example 8-2-5
Given the following truth table, find the boolean expression, and draw the logical circuit.

## Slide 41: Addition in Binary and Decimal Systems
Let’s quickly learn about how to do addition in decimal and binary systems. We all learned how to do addition in decimal number system; what about binary? How do we add 10101 and 11111 together?
First, let’s recall that binary numbers can be converted into decimal numbers:
Decimal | Binary
0 | 00
1 | 01
2 | 10
3 | 11

## Slide 42: Addition in Binary and Decimal Systems
Then, when we are doing addition in binary numbers, if we come across a number that is not a binary number, we change it from decimal to binary.
For example, we add 10101 and 11111 together, the result will be 110100.

## Slide 43: Logical Circuit of Bits Calculation
Now, we are ready to build logical circuit that does bits calculation for us. What kind of circuit can perform binary addition for us?
For example, supposed that and are 2 binary digits, then the result of + can be shown in this table:
x1 | x2 | Result of x1+x2
0 | 0 | 00
0 | 1 | 01
1 | 0 | 01
1 | 1 | 10

## Slide 44: Logical Circuit of Bits Calculation
Supposed the first bit of the result is c, and the second bit of the result is s, then we aim to create a logical circuit such that it takes x1 and x2 as input, and produce the right c and s for us.
How do we design the circuit? Well, we can work on c and s separately. First, let’s work on c.

## Slide 45: Logical Circuit of Bits Calculation
The relations between x1, x2 and c is:
By using DNF, we can easily see that
To draw this in logisim, we get:
x1 | x2 | c
1 | 1 | 1
0 | 1 | 0
1 | 0 | 0
0 | 0 | 0

## Slide 46: Logical Circuit of Bits Calculation
Now, we can work on s. The relations between x1, x2 and s is:
By using DNF, we can get
+
And this equals to . Why?
x1 | x2 | s
1 | 1 | 0
0 | 1 | 1
1 | 0 | 1
0 | 0 | 0

## Slide 47: Logical Circuit of Bits Calculation
+ = 0 + + + 0 = +
This is how we got
+ =
To draw this in logisim, we get:

## Slide 48: Half-Adder
Now, we can combine the circuit, and we get:
This is called a half-adder. It handles the addition of 2 binary numbers, and . The result is store in c and s.

## Slide 49: Full-Adder
After knowing how to design a circuit that does binary addition, how do we design a circuit that computes 111 + 111 = 1110? Consider the process of computing 111 + 111 = 1110, we know that:
1. The digit in the first 111 can be considered as .
2. The digit in the second 111 can be sonsidered as .
3. After getting the c and s from , we need to add s to the to compute the real s.

## Slide 50: Full-Adder
Then, the circuit that computes the ith digit of the result of 111 + 111 will be:
We compute of the ith digit, and we add s with so that we can find . Half Adder 2 and 3 combined are called ”Full-Adder.”

## Slide 51: 8-3 Minimization

## Slide 52: Karnaugh Map
Karnaugh map is invented by an electrical engineer, Maurice Karnaugh, in Nokia Bell Labs in 1953. (If you never hear about the Bell Labs, you should google and read about it. Tons of inventions are from this lab, such as language C, C++, Unix system, transistor, and many others.)
K-Map is used to change a truth table to its boolean expression. We learned how to do this by using DNF or CNF in chapter 8-2. However, by using DNF or CNF, we still need to minimize the boolean expression manually. By using K-Map, the result is automatically in its minimization form.

## Slide 53: Karnaugh Map
Why minimization? Well, we always want to minimize the number of gates that we use; for example, not gate, and gate, and or gate. It’s because they all take up spaces in our chips (or CPU), and they use transistors.
More gates means CPU is slower, since each gate makes the current run slower.
More gates means more electricity is needed.
More electricity means more heat our CPU generates.
Therefore, by minimizing the number of gates we use, we can make smaller, cheaper, faster, and less electricity needed, less heat-generated CPUs.

## Slide 54: Rules of Drawing K-Map
There are 4 general rules of drawing a K-Map:
Circle all 1’s and no 0’s.
The circle is a group of 1, 2, 4, 8, 16, … of 1s.
All circles must be as big as possible.
Make as few circles as possible.
Circles can go beyond the bounds of the table.

## Slide 55: Example 8-3-1
Draw K-map for the truth table below:
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 56: Example 8-3-2
Draw K-map for the truth table below: (For both orientation)
A | B | C | Output
1 | 1 | 1 | 0
1 | 1 | 0 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1

## Slide 57: Example 8-3-3
Draw K-map for the truth table below: (For just one orientation)
A | B | C | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 58: Example 8-3-4
Change the following Kmap to its boolean expression:

## Slide 59: Example 8-3-5
Change the following Kmap to its boolean expression: